## Slide 1: HSA AMD AQL PM4 profile extension API
Author: Evgeny Shcherbakov
Jun 2017

## Slide 2: Contents
Purpose
Requirements
Flow
API
Detailed API specification with simple examples

## Slide 3: Purpose
The target is to create a simple and reliable helper library, providing maximum flexibility to an HSA application which needs to gather its performance execution metrics, like hotspots, bandwidth, latency.
The library is an HSA profile extension (hsa_ven_amd_aqlprofile) and provides a C based helper API to enable a profiling of GPU compute applications. The profiling includes collecting of Performance Counters (PMC) and SQ Thread Trace (SQTT) data.
An HSA application can use the library for generating HSA_PACKET_TYPE_VENDOR_SPECIFIC AQL packets which should be submitted by the application to configure, start and stop the profiling. The library is written on C and doesn’t have direct dependencies on any infrastructure and implemented according to HSA AQL, GFX PM4 packets and the GFXIP specifications.
The generated VENDOR_SPECIFIC AQL packets carry a PM4 IB packet inside which refers to an actual PM4 commands buffer for programming GPU PMC/SQTT.

## Slide 4: Requirements
PMC/SQTT generic API
Application is aware of GPU PMC/SQTT capabilities and configurations
Application performs all memory allocations, command and PMC/SQTT output buffers
The library provides an API for querying command and PMC output buffers allocation sizes
The library is stateless. It provides the data structures and the helper methods.
The library defines its own block names. Block name is the same for a block instances set, for example each block instance from the TCC block set, TCC0, TCC1, …, TCCN will have the same block name hsa_ven_amd_aqlprofile_BLOCKS_TCC. The full name of a block instance is formed by the block name and the block index.

## Slide 5: Flow
profile object
profile object
- the profiling library API calls
STEP 2
Instantiate profile object
GPU handle
Profiling events list
Parameters list
Generate START AQL packet
Application AQL packets
Wait for the STOP AQL packet completion
Generate STOP AQL packet
STEP 1
STEP 3
STEP 4
STEP 5
Legend:
- the application task

## Slide 6: API
The library provides a generic profile context object and the following helper methods:
  instantiation of the profile context object:
    hsa_ven_amd_aqlprofile_get_info – to get command and PMC buffers sizes
  populating of start and stop AQL packets:
    hsa_ven_amd_aqlprofile_start – populating the START AQL packet
    hsa_ven_amd_aqlprofile_stop – populating the STOP AQL packet
    hsa_ven_amd_aqlprofile_legacy_get_pm4 – converting of the profiling AQL packet to PM4 packet, GFX8 support
  getting profiling output data:
    hsa_ven_amd_aqlprofile_get_info - method for getting PMC results
    hsa_ven_amd_aqlprofile_iterate_data - method for iterating the events output data samples

## Slide 7: Profile context object
  typedef struct {
  hsa_agent_t agent; // GFXIP handle
  hsa_ven_amd_aqlprofile_event_type_t type; // Events type
  hsa_ven_amd_aqlprofile_event_t * events; // Events array
  uint32_t event_count; // Events count
  hsa_ven_amd_aqlprofile_parameters_t * parameters; // Parameters array
  uint32_t parameter_count; // Parameters count
  hsa_ven_amd_aqlprofile_descriptor_t output_buffer; // Output data buffer
  hsa_ven_amd_aqlprofile_descriptor_t command_buffer; // PM4 commands buffer
  } hsa_ven_amd_aqlprofile_t;

## Slide 8: AQL packets populating
  hsa_status_t hsa_ven_amd_aqlprofile_start(
  const hsa_ven_amd_aqlprofile_t * profile, // [in] profile context object
  hsa_ven_amd_aqlprofile_packet_t * aql_start_packet); // [out] profile start AQL packet
  hsa_status_t hsa_ven_amd_aqlprofile_stop(
  const hsa_ven_amd_aqlprofile_t * profile, // [in] profile context object
  hsa_ven_amd_aqlprofile_packet_t * aql_stop_packet); // [out] profile start AQL packet
  hsa_status_t hsa_ext_legacy_get_pm4(
  hsa_ven_amd_aqlprofile_packet_t * aql_packet, // [in] AQL profile start/stop packet
  void * pm4); // [out] profile legacy PM4 packet blob

## Slide 9: Getting the profile info
  typedef union {
  hsa_ven_amd_aqlprofile_INFO_COMMAND_BUFFER_SIZE, // get_info returns uint32_t value
  hsa_ven_amd_aqlprofile_INFO_PMC_BUFFER_SIZE, // get_info returns uint32_t value
  hsa_ven_amd_aqlprofile_INFO_PMC_DATA, // get_info returns PMC uint64_t value
  // in info_data_t object
  hsa_ven_amd_aqlprofile_INFO_SQTT_DATA // get_info returns SQTT buffer ptr/size
  // in info_data_t object
  } hsa_ven_amd_aqlprofile_info_type_t;
  hsa_status_t hsa_ven_amd_aqlprofile_get_info(
  const hsa_ven_amd_aqlprofile_t * profile, // [in] profile context object
  hsa_ven_amd_aqlprofile_info_type_t attribute, // [in] requested profile attribute
  void * value); // [in/out] returned value

## Slide 10: Iterating the events output data samples
  hsa_status_t (*hsa_ven_amd_aqlprofile_data_callback_t)(
  hsa_ven_amd_aqlprofile_info_type_t info_type, // [in] data type. PMC or SQTT data
  hsa_ven_amd_aqlprofile_info_data_t * info_data, // [in] info data object
  void * callback_data); // [in/out] data pointer passed to the callback
  hsa_status_t hsa_ven_amd_aqlprofile_iterate_data(
  const hsa_ven_amd_aqlprofile_t * profile, // [in] profile context object
  hsa_ven_amd_aqlprofile_data_callback_t callback; // [in] callback to iterate the output data
  void * data); // [in/out] data passed to the callback

## Slide 11: profile_info_data structure
  typedef struct {
  uint32_t sample_id; // PMC sample or SQTT buffer index
  union {
  struct {
  hsa_ven_amd_aqlprofile_event_t event; // PMC event
  uint64_t result; // PMC result
  } pmc_data;
  hsa_ven_amd_aqlprofile_descriptor_t sqtt_data; // SQTT output data descriptor
  };
  } hsa_ven_amd_aqlprofile_info_data_t;

## Slide 12: Profile data callback
typedef struct {
uint32_t sample_id; // PMC sample or SQTT buffer index
union {
struct {
hsa_ven_amd_aqlprofile_event_t event; // PMC event
uint64_t result; // PMC result
} pmc_data;
struct {
void * ptr; // pointer on SQTT output data
uint32_t size; // size of SQTT output data
} sqtt_data;
};
} hsa_ven_amd_aqlprofile_info_data_t;

## Slide 13: Detailed API specification with PMC and SQTT profiling simple examples
HSA extension profile library API Specification
rev 1.2.0

## Slide 14
Q&A