## Slide 1: AMD GPU Performance API PAPI interfacing
Author: Evgeny Shcherbakov
NOV 2017

## Slide 2: ROCM Profile library
The goal of the implementation is to provide a HW specific performance analysis interface for profiling of GPU compute applications
The profiling includes HW performance counters (PMC) with complex performance metrics and thread traces (SQTT). The implementation distinguishes two profiling features, metrics and traces
Basic metrics and complex metrics as expressions on the basic metrics are supported.
The library will be used by AMD specific profiling tools or by higher level HW independent performance analysis API like PAPI and open source tools like TAU/Eclipse PTP
The library provides C based API.
Supports two usage modes, HSA API intercepting for per kernel data collection and standalone mode for perf-counters sampling
Currently we have prototyping implementation but the library still in development stage
Going to be open sourced

## Slide 3: ROCm PL Requirements 1
Provide profiling based on the following HW profiling features:
  Performance counters in accumulating mode (PMC)
  SQ Thread Trace (SQTT)
Provide a C based profiling API:
  API to query the list of supported metrics and their properties, name/id conversion.
  start/stop/read API
  Callback API for enabling profiling for the kernels dispatched to HSA AQL queues.
Two basic usage models:
  Per kernel profiling data collecting using dispatch callback API
    Loaded by HSA-runtime as a tool library. Actual profiler tool lib is loaded by ROC profiler.
  Statistical profiling, sampling in standalone mode
The library is responsible for allocation of the buffers for profiling.
The library API is abstracted from the specific GFXIP.

## Slide 4: ROCm PL Requirements 2
Automatically identify required number of the application runs and metric group per each run to collect all data needed for all specified metrics.
The library implementation is configurable, flexible and extensible:
  Easy adding of counters and metrics, counters/metrics enumeration and id/name conversion API
  Counters and metrics can be dynamically configured using XML configuration files:
    Counters entry: counter name, block name, event id
    Complex metric entry: metric name, expression from basic metrics
    GFXIP specific basic metrics and GFXIP abstracted complex metrics
      Basic metrics GFXIP specific examples, amount of data, stalls number, cycles number
      Complex GFXIP gnostic metrics: memory bandwidth, bus efficiency
    XML configuration will support GFXIP specific and global namespaces

## Slide 5: Metrics XML file example
Current prototype version
<gfx8>
<metric name=L1_CYCLES_COUNTER block=L1 event=0 >
<metric name=L1_MISS_COUNTER block=L1 event=33 >
. . .
</gfx8>
<gfx9>
. . .
</gfx9>
<global>
<metric name=L1_MISS_RATIO expr=L1_CYCLES_COUNT/ L1_MISS_COUNTER ></metric>
</global>

## Slide 6
Another considered variant:
<gfx8>
<L1>
<event name=CYCLES id=0 >
<event name=MISS event=33 >
. . .
</L1>
. . .
</gfx8>
<global>
<metric name=L1_MISS_RATIO expr=L1.CYCLES/ L1.MISS ></metric>
</global>

## Slide 7: Usage
HSA application
HSA ProxyQueue interface
HSA runtime
ROC Profiler lib
loaded by HSA runtime
Profiling Tool
Per kernel profiling mode, application context
ROC Profiler library is loaded by hsa-runtime. ROC profiler is intercepting the HSA AQL queue create API and provides a dispatch callback interface for the profiling tool.

## Slide 8
AQL Profile API
HW counters start/stop/sample
Profiling tool context
HSA AQL Queue interface
HW independent API
PAPI Preset events - predefined events, are a common set of events deemed relevant and useful for application performance tuning.
Performance API
(PAPI)
ROC Profiler lib
Profiling Tool
(TAU/Eclipse PTP)
HSA runtime
High-Level Language
runtime
HSA application context
HSA runtime
  Statistical profiling / sampling, tool context.

## Slide 9: API overview
Object oriented
  Profiling context is a main profiling container which supports needed for profiling buffers, for output data and command packets
  API supports different types of complexity with one global context or with global resources tracker which synchronize different contexts
Info API – iterating available profiling features, metrics, traces and their parameters
Context API
  open/close/get_groups – creating/destroying profiling context and getting identified profiling groups
  get_data - getting/waiting-for the counters groups data
  get_metrics – calculating the registerd to the context metrics
  start/stop/read – profiling in standalone mode using a specific queue
  dispatch_callback – pre-kernel profiling data collecting
  get_error_string
  Global log supporting /tmp/rocprofiler_log.txt

## Slide 10: ROC Profiler PROTOTYPE specification
ROC Profiler Library Specification

## Slide 11
Q&A